## Slide 1: CST21123 计算机组成与结构
刘大江
计算机学院
Lab 2：存储器与控制器实验
2024春季

## Slide 2: 实验原理图
Add
S
PC
Imm
Gen
Inst[31:0]
Instruction
memory
Read
address
25
32
4
Main
Control
Branch
MemRead
RegSrc
ALUOp
MemWrite
ALUSrc
RegWrite
ImmSel
Inst[6:0]
Inst[31:7]
ALU
control

## Slide 3: 带控制的RISC-V数据通路
Add
S
Add
Sum
PC
Imm
Gen
M
U
X
0
1
M
U
X
0
1
Inst[31:0]
Instruction
memory
Read
address
ALU
result
Less
Zero
Registers
Read
Register1
Read
Register2
Write
Register
Write
data
Read
data1
Read
data2
Data
memory
Address
Read
data
Write
data
25
32
4
Shift
left1
M
U
X
1
0
Main
Control
Branch
MemRead
RegSrc
ALUOp
MemWrite
ALUSrc
RegWrite
ImmSel
Inst[6:0]
Inst[19:15]
Inst[24:20]
Inst[11:7]
Inst[31:7]
ALU
control

## Slide 4: RISC-V 指令类型回顾
所有的指令类型都需要用到 ALU 吗？

## Slide 5: ALU 的控制
ALU 的用途
  在 load/store （I/S）指令中用作 ADD
  在分支指令中（B）用作比较（SUB?）
  在 R/I 类算术逻辑指令中，其功能由指令的func字段决定
  在 LUI 指令中用作旁路
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract

## Slide 6: ALU 的控制
Function 只需要输入 4 bits.
opcode | ALUOp | Operation | Function field | ALU function | ALU control
ld | 00 | load register | xxxxxxxxxx | ADD | 0001
sd | 00 | store register | xxxxxxxxxx | ADD | 0001
branch | 01 | BEQ | xxxxxxx000 | SUB | 0010
arith. | 10 | ADD[I] | 0000000000 | ADD | 0001
 |  | SUB | 0100000000 | SUB | 0010
 |  | AND[I] | 0000000111 | AND | 0011
 |  | OR[I] | 0000000110 | OR | 0100
 |  | XOR[I] | 0000000100 | XOR | 0101
 |  | SLL[I] | 0000000001 | SLL | 0110
 |  | SRL[I] | 0000000101 | SRL | 0111
 |  | SRA[I] | 0100000101 | SRA | 1000
 |  | SLT[I] | 0000000010 | SLT | 1001
ALU control
function
ALUOp
ALUCtrl
4bits
2 bits
4 bits

## Slide 7: ALU 的数据通路实现(Zero)
/* implement here */
Always @(*) begin
Zero_o = (data1_i - data2_i)?0:1;
case(ALUCtrl_i)
PASS: begin data_o = data2_i; end
SUM : begin
data_o = data1_i + data2_i;
end
SUB : begin
data_o = data1_i - data2_i;
end
AND : begin
data_o = data1_i & data2_i;
end
…
…
OR : begin
data_o = data1_i | data2_i;
end
XOR : begin
data_o = data1_i ^ data2_i;
end
MUL : begin
data_o = data1_i * data2_i;
end
default : begin
data_o = data1_i;
end
endcase
end

## Slide 8: ALU 控制器 Verilog 实现
module ALU_Control(
input [3:0] funct_i,
input [1:0] ALUOp_i,
output ALUCtrl_o)
reg[3:0] ALUCtrl_o
always@(*)begin
case(ALUOp_i)
2’b11 : begin
ALUCtrl_o = 3’b000;// bypass
end
2'b10 : begin //reg-reg / reg-imm
case(funct_i)
4’b0000 : begin
ALUCtrl_o = 4’b0001;//add
end
4'b1000 : begin
ALUCtrl_o = 4’b0010;//sub
end
4'b0110 : begin
ALUCtrl_o = 4’b0100;//OR
end
4'b0111 : begin
ALUCtrl_o = 4’b0011;//AND
end
...
endcase
end
2’b01 : begin //beq, ALU do subtraction
ALUCtrl_o = 4’b0010; //sub
end
2’b00 : begin //lw or sw
ALUCtrl_o = 4’b0001; //add
end
endcase

## Slide 9: 主控制器
 | 立即数格式 | 扩展方式
I | [31:20] | 有符号位扩展
S | [31-25,11-7] | 有符号位扩展
B | [31,7,30-25,11-8] | 有符号位扩展
J | [31,19-12,20,30-21] | 有符号位扩展
opcode | ALUOp
ld | 00
sd | 00
branch | 01
arith. | 10
bypass | 11
Add
S
Add
Sum
PC
Imm
Gen
M
U
X
0
1
Inst[31:0]
Instruction
memory
Read
address
25
32
4
Shift
left1
Main
Control
Branch
MemRead
RegSrc
ALUOp
MemWrite
ALUSrc
RegWrite
ImmSel
Inst[6:0]
Inst[31:7]
ALU
control

## Slide 10: 构建主控制器真值表(算术逻辑)
op | Inst[6:0] | Branch | MemRead | RegSrc | MemWrite | ALUOp | ALUSrc | RegWr. | ImmSel
add | 7’h33 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b0 | 1’b1 | *
addi | 7’h13 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b1 | 1’b1 | I
sub | 7’h33 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b0 | 1’b1 | *
and | 7’h33 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b0 | 1’b1 | *
andi | 7’h13 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b1 | 1’b1 | I
or | 7’h33 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b0 | 1’b1 | *
ori | 7’h13 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b1 | 1’b1 | I
xor | 7’h33 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b0 | 1’b1 | *
xori | 7’h13 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b1 | 1’b1 | I
sll | 7’h33 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b0 | 1’b1 | *
slli | 7’h13 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b1 | 1’b1 | I
srl | 7’h33 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b0 | 1’b1 | *
srli | 7’h13 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b1 | 1’b1 | I
sra | 7’h33 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b0 | 1’b1 | *
srai | 7’h13 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b1 | 1’b1 | I
slt | 7’h33 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b0 | 1’b1 | *
slti | 7’h13 | 1’b0 | 1’b0 | 1’b0 | 1’b0 | 2’b10 | 1’b1 | 1’b1 | I
 | 立即数格式 | 扩展方式
I | [31:20] | 有符号位扩展
S | [31-25,11-7] | 有符号位扩展
B | [31,7,30-25,11-8] | 有符号位扩展
J | [31,19-12,20,30-21] | 有符号位扩展

## Slide 11: 构建主控制器真值表(访存/分支)
OP | Inst[6:0] | Branch | MemRead | RegSrc | MemWrite | ALUOp | ALUSrc | RegWr. | ImmSel
LW | 7’h03 | 1’b0 | 1’b1 | ’b1 | 1’b0 | 2’b00 | 1’b1 | 1’b1 | I
SW | 7’h23 | 1’b0 | 1’b0 | * | 1’b1 | 2’b00 | 1’b1 | 1’b0 | S
BEQ | 7’h63 | 1’b1 | 1’b0 | * | 1’b0 | 2’b01 | 1’b0 | 1’b0 | B
BranchType | Code
BEQ | 3’b001
BNE | 3’b010
BGE/BGEU | 3’b011
BLT/BLTU | 3’b100
JALR/JAL | 3’b101
Non-Branch | 3’b000
 | 立即数格式 | 扩展方式 | 编码
I | [31:20] | 有符号位扩展 | 000
IU | [31:20] | 无符号扩展 | 001
S | [31-25,11-7] | 有符号位扩展 | 010
B | [31,7,30-25,11-8] | 有符号位扩展 | 011
U | [31-12] | <<12 | 100
J | [31,19-12,20,30-21] | 有符号位扩展 | 101
opcode | ALUOp
ld | 00
sd | 00
branch | 01
arith. | 10
Bypass | 11

## Slide 12: RV32I只用到9-bit的ISA
op | Inst[6:0] | Inst[6:0]
add | 7’h33 | 7’b0110011
addi | 7’h13 | 7’b0010011
sub | 7’h33 | 7’b0110011
and | 7’h33 | 7’b0110011
andi | 7’h13 | 7’b0010011
or | 7’h33 | 7’b0110011
ori | 7’h13 | 7’b0010011
xor | 7’h33 | 7’b0110011
xori | 7’h13 | 7’b0010011
sll | 7’h33 | 7’b0110011
slli | 7’h13 | 7’b0010011
srl | 7’h33 | 7’b0110011
srli | 7’h13 | 7’b0010011
sra | 7’h33 | 7’b0110011
srai | 7’h13 | 7’b0010011
slt | 7’h33 | 7’b0110011
slti | 7’h13 | 7’b0010011
sltu | 7’h33 | 7’b0110011
sltiu | 7’h13 | 7’b0010011
OP | Inst[6:0] | Inst[6:0]
LW | 7’h03 | 7’b0000011
SW | 7’h23 | 7’b0100011
BEQ | 7’h63 | 7’b1100011
BGE | 7’h63 | 7’b1100011
BGEU | 7’h63 | 7’b1100011
BLT | 7’h63 | 7’b1100011
BLTU | 7’h63 | 7’b1100011
BNE | 7’h63 | 7’b1100011
JAL | 7’h6f | 7’b1101111
JALR | 7’h67 | 7’b1100111
AUIPC | 7’h17 | 7’b0010111
LUI | 7’h37 | 7’b0110111
Inst[30]
Inst[14:20]
Inst[6:2]

## Slide 13: 基于组合逻辑的主控制器实现
always@(*)begin
case(inst[6:2])
5’b01100: begin //R-type
BrachType = 1’b0;
MemRead = 1’b0;
RegSrc = 1’b0;
MemWrite = 1’b0;
ALUOp = 2’b10;
ALUSrc = 1’b0;
RegWrite = 1’b1;
ImmSel <= *;
end
5’b0100: begin /Imm-Type
BrachType = 1’b0;
MemRead = 1’b0;
RegSrc = 1’b0;
MemWrite = 1’b0;
ALUOp = 2’b10;
ALUSrc = 1’b1;
RegWrite = 1’b1;
ImmSel <= I;
end
...
addi | 7’h13 | 3’b000 | 1’b0 | 2’b00 | 1’b0 | 2’b10 | 1’b1 | 1’b1 | I
… | … | … | … | … | … | … | … | … | …
sltiu | 7’h13 | 3’b000 | 1’b0 | 2’b00 | 1’b0 | 2’b10 | 1’b1 | 1’b1 | IU

## Slide 14: 完整的数据通路+控制通路
Add
S
Add
Sum
PC
Imm
Gen
M
U
X
0
1
Inst[31:0]
Instruction
memory
Read
address
25
32
4
Shift
left1
Main
Control
Branch
MemRead
RegSrc
ALUOp
MemWrite
ALUSrc
RegWrite
ImmSel
Inst[6:0]
Inst[31:7]
ALU
control
Inst[30,14:12]